## Slide 1: IP Multimedia Subsystem

## Slide 2: Change of service perception paradigm
SMS
MMS
VoIP
DVB-H
Voice
Low speed data
modems (V.90)
Old – Network centric oriented
New – User centric oriented
+ other PC and software
smtp
ftp
http
Services

## Slide 3: Pohľad na služby
Customers are people – they want it all, now!
  Any & all media (voice, video, data, web …)
  Any & all terminal (phone, PDA, laptop, cell phone …)
  Any & all network (POTS, ISDN, IP, WiFi, GPRS, UMTS …)
  Any & all time
  Any & all places
  1 to 1 or 1 to many
  Mixing synch & asynch
  Security
  Quality
  affordable

## Slide 4: - Internet
- „Classical“ public telephony network - PSTN
User
User
Selected
server
Selected
server
Internet
“Dumb net”
R
R
R
R
Central
Control
User
User
Central
Control
Central
Control
SW
SW
SW
SW
SW
SW
UNI
NNI
NNI
UNI
Different worlds...
QoS is supported natively
Internet = „best effort“
Pushing the value outside the network
...
How to remain in the value chain?
... Strong innovanitess in strategy

## Slide 5
  NGN – softswitch architektúra
oddelenie vrstvy služieb od riadiacej a transportnej vrstvy
paketový prenos dát
otvorené a normalizované rozhrania medzi jednotlivými vrstvami
podpora viacnásobných aplikácií cez rôzne prístupové siete a koncové zariadenia
IETF

## Slide 6
  NGN – softswitch architektúra - implikácie
Telefonica DE

## Slide 7: Charakteristiky NGN, ktoré by mala spĺňať:
Oddelenie riadiacich funkcií od prenosových vlastností. Oddelenie poskytovania služieb od siete a zabezpečenie prístupu cez otvorené rozhrania a tým flexibilnú, otvorenú a distribuovanú architektúru.
Vysokokapacitný paketový prenos v rámci prenosovej infraštruktúry, avšak s možnosťou pripojiť existujúce i budúce siete (či už siete s prepínaním paketov, siete s prepínaním okruhov, spojovo, či nespojovo orientované, pevné aj mobilné)
Podporu pre široké spektrum služieb a aplikácií s použitím mechanizmov založených na modulárnej a flexibilnej štruktúre stavebných blokov elementárnych služieb
Konvergované služby medzi pevnými a mobilnými sieťami (taktiež konvergenciu hlasu, dát a videa). Rôzne kategórie služieb s potrebou rozdielnych QoS a tried služieb (CoS)
Nezávislosť evolúcie služieb od používanej transportnej infraštruktúry
Rôzne typy mobility (používateľov, terminálov, služieb). Neobmedzený prístup používateľov k rôznym poskytovateľom služieb
Jednotný riadiaci protokol – SIP (Session Initiation Protocol)
Dodržanie regulačných požiadaviek ako napríklad núdzové volania a bezpečnostné požiadavky pri zachovaní ochrany osobných údajov
Lacnejšie a efektívnejšie technológie v porovnaní so súčasnými technológiami
NGN

## Slide 8: Standarts: Path to IMS
Standarts: Path to IMS

## Slide 9
  NGN – prehľad softswitch architektúry

## Slide 10
  Modern architectures for modern services
IMS – the Standart for Converging Networks

## Slide 11
Visited
Network
IMS Home Network - Functional Elements
HSS
DNS
ENUM
I-CSCF
S-CSCF
Home Network
AS
AS
AS
Home Subscriber Server
Centralized DB
HLR successor
User profile
Filter criteria (sent to S-CSCF)
  Which applications
  Which conditions
Application Servers
Push-to-talk
Instant messaging
Telephony AS
3rd party or IMS Vendor
Domain Name Server
P-CSCF
MGCF
MGW
PSTN
H.248
ISUP
BGCF
SIP
SS7
SIP
SIP
SIP
SIP
SIP
SIP
SIP
Diameter
RTP
TDM
Call Session
Control Function
SIP registration
SIP session setup
MS
MS
MRFC
Media Gateway Control Function
Interfaces to PSTN/PLMN by
  Converting SIP <-> ISUP
  Interworking RTP to circuit
H.248 control of MGW
Breakout Gateway Control Function
Selects network (MGCF or other BGCF) in which PSTN/ PLMN breakout is to occur
Media Resource Function Controller
Pooling of Media servers (e.g. conference)
Proxy CSCF
1st contact point for UA
QoS
Routes to S-CSCF
Interrogating CSCF
Entry point for incoming calls
Determines S-CSCF for Subscribers
Hides network topology
Serving CSCF
Registrar
Session control
Application Interface
P-CSCF
SIP
SIP
UA/UE
UA/UE
Architektúra NGN, SSW a IMS
Notes: This slide shows a single network topology using IMS. A call originating from a SIP User Agent in the IMS network may go to another SIP UA or egress to the PSTN.
The HSS contains all of the subscriber information. In the wireless network it is the evolution of the HLR. In the wireline network it is the equivalent of customer records provisioned on switches.
Application Servers are where the application reside. There may, for example, be originating services or terminating services. The filtering criteria is loaded into the S-CSCF when the subscriber registers with the network.
DNS is used to identify elements use in the session set up.
The CSCFs manage the session control: registration, set up, tear down, feature activation.
The P-CSCF is first point of interaction with the User Agent. It also manages Quality of Service and other conditions specific to a UA.
The I-CSCF is used in network to network signaling. The I-CSCF hides the network topology from an external network.
The S-CSCF is the primary signal processing engine in IMS. It manages registration, checks for triggers for services and performs routing (although routing instructions may come from Application Servers).
Media Resources may be conference services, IVRs or other network services.
If a call must egress to the PSTN the BGCF selects the appropriate Media Gateway that can be used.
Media Gateways control the conversion from IP to PSTN TDM signaling. Media Gateway Control Functions control the signaling between IMS and the PSTN (e.g. IP to SS7).

## Slide 12
  NGN – IMS funkčná architektúra
Border & Media Control
Applications
SGW
Media Services
P/I-CSCF
Access
PSTN/
PLMN
THIG
MGCF/
MGW
Subscriber
Application Servers
Mobile Features
Application Servers
SCIM
Session Control
HSS
S-CSCF
BGCF
Other VoIP Network
Mgt. & Charging

## Slide 13
  NGN – funkčné entity IMS architektúry
CSCF — Call Session Control Function
PROXY-CSCF — The P-CSCF is the first entry point for the user equipment (UE) into the IMS.
INTERROGATING-CSCF — The I-CSCF is used for initially choosing the correct S-CSCF.
SERVING-CSCF — The S-CSCF handles call session state in the IMS, including coordinating the use of Application Servers for enhanced services. Also, it is the subscriber registrar and is always in the home network.
BGCF —The Breakout Gateway Control Function routes calls to the public switched telephone network (PSTN) or any other circuit-based network.
MGCF/MGW — The Media Gateway Control Function/ Media Gateway handles media to and from the PSTN.
SGW - The Signaling Gateway passes circuit-based signaling to and from the PSTN.
AS — An Application Server (i.e., SIP AS, OSA AS, or CAMEL IM-SSF) offers value-added services and resides in the user’s home network or in a third party location. An AS based in the home network can access the HSS as needed.
HSS — The Home Subscriber Server is the master database for subscriber data, containing subscription-related information to support call processing network entities. The HSS interfaces with call control servers in order to complete routing/roaming procedures by authentication, authorization, naming/ addressing resolution, location dependencies, etc.

## Slide 14: IMS vývoj
Vyvinul sa v mobilných sieťach (ako 3GPP štandard)
2G siete podporovali (takmer iba) prenos hlasu (circuit-switch) aplikácie
3G siete mali natívnu podporu pre prenos dát pomocou paketov
Používatelia majú prístup k rýchlemu Internetu
=> Používatelia už nepotrebujú hlasové služby od operátora!!!

## Slide 15: Prečo nepoužívame Internet
Internet poskytuje všetko
  VoIP lacné telefonovanie
  Služby spojené s ISDN
Prečo potrebujeme NGN?
Internet neposkytuje:
  Garanciu QoS
  Spoplatnenie
  Možnosť integrácie rôznych služieb

## Slide 16: Naozaj potrebujeme QoS
Väčšinou funguje dobre
Niekedy nefunguje vôbec...
Neprípustné pre firmy
Riadenie QoS je aj o užívaní si služby s garanciou kvality ako o hnevaní sa s lacnou službou
V súčasnom Internete nie je snaha rozlišovať služby

## Slide 17: Naozaj potrebujeme Spoplatnenie?
Vytvoriť „spravodlivý“ model spoplatnenia
Keď používateľ pozná obsah dát, môže zvýhodniť istú službu (Videokonferenciu napr.) aj keď by bola štandardne veľmi drahá
Náklady sú fixné, príjmy sa odvíjajú od skonzumovaných služieb
NGN nenúti použitie konkrétneho spoplatňovacieho modelu
Napr. spoplatnenie IM bez ohľadu na množstvo prenesených dát, spoplatnenie mult. relácie na základe trvania

## Slide 18: Naozaj potrebujeme Integrované služby?
Multimediálne služby už nestačia
Cieľom je mať otvorené prostredie na vývoj aplikácií a ich vzájomnú integráciu
Keď mi príde voice-mail, chcem informáciu e-mailom
Operátori chcú poskytovať aj internetové služby
Tieto služby musia fungovať rovnako dobre v roamingu ako aj v domácej sieti
Moja služba funguje (relácia) bez ohľadu na prístupovú technológiu (má informácie o nej)
Služby by mali navyše fungovať medzi Internet používateľom a IMS používateľom

## Slide 19: IMS - protokoly
SIP
Diameter
RTP a RTCP

## Slide 20
  NGN – IMS architektúra
Tispan

## Slide 21: Identity v IMS
V PSTN bola identita jedna.
Verejná identita
  sip:meno.priezvisko@operator.sk
  sip:+421-902-111222@operator.sk
  tel:+421-902-111222
  Tel uri nemôže byť registrované v SiP serveri
Privátna identita
  meno@operator.sk
  Je používaná iba pre autentifikáciu a identifikáciu používateľov
  Používateľ zvyčajne nepozná (ako IMSI)
  Nomôže sa používať pre potreby SIP signalizácie

## Slide 22: Relations between Identities
IMS
Subscriber
Private
UID 2
Private
UID 1
Public
UID 1
Public
UID 3
Public
UID 2
Public
UID n
.
.
.
}
Implicit Set

## Slide 23
Tispan
RNC
MSC(Server)
SGSN
GGSN
CN
MGW
BSC
UMTS/GPRS
WLAN
Corporate
P-CSCF
I-CSCF
MRF
MGW
MGCF
IMS
S-CSCF
SIP Application
Servers
SIP Application
Servers
HSS
CDMA 2000
DSL/Cable Modem
DSLAM/CMTS

## Slide 24: Registration procedure 1
www.tech-invite.com

## Slide 25: Registration procedure 2
www.tech-invite.com

## Slide 26: Registration procedure 3
www.tech-invite.com

## Slide 27: Registration procedure 4
www.tech-invite.com

## Slide 28
Control
Bearer
Called Party
Visited Network
Called Party
Home Network
Calling Party
Home Network
Calling Party
Visited Network
UE
P-CSCF
HSS
S-CSCF
SIP
SIP
Diameter
UE
P-CSCF
AS
HSS
S-CSCF
SIP
AS
SIP
Diameter
I-CSCF
Diameter
DNS
Backbone
Packet
Network
RAN
Backbone
Packet
Network
RAN
Initiate SIP Invitation
1
1
Retrieve Subscriber Profile (if needed)
2
2
3
3
Apply Service Logic
Retrieve Address of CLD Party Home Network
and Forward INVITE.
4
4
Identify Registrar of CLD Party and Forward INVITE.
5
5
Retrieve Subscriber Profile (if needed)
6
6
7
7
Apply Service Logic
Forward INVITE to CLD Party
8
8
Ringing / Alerting
10
10
IMS Subscriber to IMS Subscriber high level call flow
SDP Negotiation / Resource Reservation Control
9
9
RTP Stream
Answer / Connect
11
11
Architektúra NGN, SSW a IMS

## Slide 29: Hovor 1

## Slide 30: Hovor 2

## Slide 31: Filtering
Only initial SIP requests
Initial filter criteria (iFC) retrieved from HSS
during registration
Subsequent filter criteria (sFC) provided by application server (beyond 3GPP R8)
  Allow dynamic definition of trigger points during application runtime

## Slide 32: Example: Presence call flow
Service profile
  assigned to users that want to use presence
IFC
  AS: Presence Server
  TP: CNF (&)
    Method and
      PUBLISH or
      SUBSCRIBE
    Event
      Header: Event
      Content: .*presence.*
P-CSCF
Presence
Server
S-CSCF
SUBSCRIBE
200 OK
200 OK
NOTIFY
SUBSCRIBE
200 OK
200 OK
NOTIFY
SUBSCRIBE
200 OK
200 OK
NOTIFY
UE